## Slide 1: Wireless Ad Hoc Networks Lab 1
Wireshark
Packets Sniff Experiment

## Slide 2: Open VM VirtualBox - Setting

## Slide 3: Isolate wireless USB adapter

## Slide 4: VirtualBox Start
Password : ImBun

## Slide 5: Check wireless USB adapter has been driven or not?
Open terminal
iwconfig
Check wireless USB adapter has been driven. (If not, change USB port.)

## Slide 6: Check wireless USB adapter has been driven or not?

## Slide 7: Packets Sniff Experiment
Lab Purpose
  Understand wireless network by capturing packets.
Equipments
  PC / NB ( Root Password : ImBun )
  Atheros-chipset wireless NIC (support IEEE 802.11 b/g)
  Linux with iw (linux wireless package)
  Wireshark (network protocol analyzer)
  WiFi Access Point (Open Access / Encrypted)

## Slide 8: Wireshark Introduction
A Free and Open-Source Packet Analyzer
Available for UNIX and Windows
  https://www.wireshark.org/
Capture live packet data from a network interface
Purpose:
  Network Administrators : troubleshoot network problems
  Network Security Engineers : examine security problems
  Developers : debug protocol implementations
  People : learn network protocol internals
Installation on Ubuntu
  sudo apt-get install wireshark
  sudo wireshark
Notes: sudo apt-get update
sudo apt-get install wireshark
sudo groupadd wireshark
sudo usermod -a -G wireshark bunlab
sudo chgrp wireshark /usr/bin/dumpcap
sudo chmod 750 /usr/bin/dumpcap
sudo setcap cap_net_raw,cap_net_admin=eip /usr/bin/dumpcap
sudo getcap /usr/bin/dumpcap

## Slide 9: Wireshark Installation (from source)
Package Download Link :
https://1.as.dl.wireshark.org/src/wireshark-2.2.2.tar.bz2
Open the terminal, then type these commands:
  Unpack the source file:
  tar xaf wireshark-1.12.8.tar.bz2
  Go to the Wireshark source directory:
  cd wireshark-2.2.2
  configure the source:
  ./configure
  Build the source:
  make
  Install:
  make install

## Slide 10: Wireshark User Interface (I)

## Slide 11: Wireshark User Interface (II)

## Slide 12: Linux Introduction w/ network command
ifconfig - configure a network interface
  Set IP address, MAC address … etc

## Slide 13: Linux Introduction w/ wireless network command
iwconfig - configure a wireless network interface
  Set ESSID, channel, rate …etc

## Slide 14: Wireless Operating Modes
Wi-Fi modes of operation (802.11 or Wi-Fi)
  Station (STA) infrastructure mode
    This mode is also called “ Managed “
  AccessPoint (AP) infrastructure mode
  Ad-Hoc (IBSS) mode
  Monitor (MON) mode (i.e, Sniff mode)
    Don’t need to connect any AP

## Slide 15: Monitor mode – Wireless Channel
Fig. 2.4 GHz Wi-Fi channels (802.11b,g WLAN)

## Slide 16: Packets Sniff Experiment
[Step 1] Install Unix-like operating system. (Done For You)
[Step 2] Download & install Wireshark. (Done For You)
[Step 3] Switch the wireless NIC to monitor mode.
  delete the normal wlan# interface if it’s unused :
  iw dev
  sudo iw dev wlan# del
  add a monitor interface called mon? :
  sudo iw phy phy# interface add mon? type monitor
  enable the mon? interface using ifconfig :
  sudo ifconfig mon? up
  specify the wireless LAN frequency you want to capture on :
  sudo iwconfig mon? channel x
  or sudo iw dev mon0 set freq 24yz
[Step 4] Open Wireshark to capture and observe the packets
  sudo wireshark (Use Wireshark with root authority)
(to list the available devices)
(change # to the specific number)
(change ? to the a number)

## Slide 17: Questions & Report
TA will use our own devices to access Internet via an AP (Open Access/Encrypted).
TA will generate HTTP, FTP, Telnet and SSH packets.
Questions:
  # Q1 :
  Can you get any detail information from received packets for HTTP, FTP,
  Telnet and SSH via Open Access AP!?
  (ex: username, password)
  # Q2 :
  Can you get any detail information from received packets for HTTP, FTP,
  Telnet and SSH via Encrypted AP!?
You need to answer these questions and then write a full report with your thoughts or analysis(individual report).
  Deadline : 2019 / 11 / 19
Notes: ftp ca.nctu.edu.tw
==================
ssh bunlab@140.113.144.197
pw : ImBun
==================
telnet ptt.cc
==================
http://bun.cm.nctu.edu.tw/labinfo/?page_id=1224
pw : ting-adhoc-2019